EMRG
OARC Meeting 2010-02-10
EMERGENCY MEASURES RADIO GROUP
OTTAWA ARES
Two Names - One Group - One Purpose
In Building Signal Reinforcement For Amateur Radio Emergency Communications
Date Of Last Change: 2010-01-30
Version: 1.0

---
Situation
Situation
In an emergency, EMRG Clients will be operating from multi-room, multi-level, commercial buildings.
  - Examples: Nepean Sportsplex, City Hall
Most commercial buildings are constructed with concrete and steel, which acts as an RF shield.
Most amateur repeaters are designed for mobile or base station use, not portable or in building use.
  - Using portables radios outside depends on location.
Emergency Measures Radio Group (EMRG) - Ottawa ARES

---
Communications Evolution
Communications Evolution
Black 500 set in the front hall has been replaced by phones in almost every room, cordless or mobile phones and more than 1 phone line.
Radio operator beside the main door with cable outside to an antenna has also been replaced.
Clients want communications co-located so information can be exchanged quickly, in real time.
May require 2 or more voice channels + data channel

---
Quality & Consistency
Quality & Consistency
QUALITY: “Better Than Nothing” = Nothing
  - If audio signal quality of 3 and above is considered usable, then providing an audio quality of 1 or 2 is viewed by clients as providing nothing.
CONSISTENCY: The capability and audio quality must be consistent through shift changes.
  - Shift 1 has cross band repeater capability so they can communicate from anywhere inside the building.
  - Shift 2 only has a portable radio so they can only communicate from outside the building.

---
Cross Band Repeaters
Cross Band Repeaters
Cross band repeaters offer excellent solution to extend coverage to portable radios inside.
Can be deployed to any building
Problem with consistency if cross band mobile is in a vehicle and the person leaves.
Establishing multiple voice channels for a single building becomes more challenging due to the amount of equipment and interference between systems.

---
Two EMRG Challenges Two Different Solutions
Two EMRG Challenges
Two Different Solutions
Ottawa City Hall
Emergency Operations Centre (EOC)
Ben Franklin Plan
Emergency Social Services (ESS) Command Centre

---
City Hall EOC
City Hall EOC
OBJECTIVE:
Provide up to 3 voice channels and 1 data channel in the EOC using portable radios, so the radio operator can sit at any position in the EOC.
Video Screens
Entrance
RADIOS
Supply Storage
Emergency
Exit

---
In Band & Cross Band Repeater Extension
In Band & Cross Band Repeater Extension
VOICE CHANNELS
VHF – VHF
UHF – UHF
UHF – 220
Penthouse Roof
Penthouse Mechanical Rooms
5
4
3
Floors…2
EOC - Main Floor City Hall
Not To Scale
Portable
Radio
50 Ft Vertical separation from EOC to Roof = 50 db isolation + isolation from concrete and steel in 5 floors of building.
Radio 2
To/From EMRG Repeaters
Medium Power (10W)
Antenna On EOC Ceiling
Radio 1
Controller
Low Power
In-Band Repeater

---
Antenna on wire mesh for isolation from voice antenna
Tri-band (144/220/440)
PENTHOUSE ROOF
INSIDE EOC
CHANNEL 1
VHF
VHF
Multi Channel
Controller
Dual-band Mobile Antenna In Ceiling
CHANNEL 2
UHF
UHF
Multi Channel
Controller
CHANNEL 3
Dual-band Mobile Antenna In Ceiling
UHF
220 MHz
Multi Channel
Controller
DATA
WiFi 2.4 GHz on EOC Ceiling
VHF
Multi Channel
Computer
TNC
UPS
Triplexer
Diplexer
1
2
3
4
W

---
Ben Franklin Place (BFP)
Ben Franklin Place (BFP)
OBJECTIVE:
Provide 3 voice channels and 1 data channel using portable radios in BFP, & 100 Constellation, and extending to Algonquin College.

---
Multi Coupling +  Cross Band Repeaters
Multi Coupling +
Cross Band Repeaters
Ben Franklin Place
NCS
Red Cross
City EOC.
Reception Centres would typically use VHF only
UHF Repeater
UHF
Repeater Frequency
Repeater Frequency
VHF
UHF
VHF Repeater
VHF
EMRG UHF Cross band Frequency #2
Cross Band
Repeater
220
UHF
220
Simplex
EMRG UHF Cross band Frequency #3
Cross Band
Repeater
UHF
VHF
UHF
Digi
Simplex
VHF
Outpost & Winlink
UHF Packet Frequency

---
SG-301 (SRL-301)
UHF Omni
220 Omni
SG-201 (SRL 201)
VHF Omni
VHF
Multi-Channel
UHF
CH2
Controller
220
UHF
CH3
Controller
UHF
Data
TNC
CH1
Kenwood TKR-850
X

---
Remote Channel Control
Remote Channel Control
Remote channel selection
Local Repeaters, or Simplex Frequency
DTMF
Control
UHF Radio
VHF Radio
Radio User inside the building
Controller
1
2
3
4
5
6
7
8
6
8
9
12
14
Motorola Radius GM300
16 pin accessory connector
Diodes = 1N914 or equivalent
NHRC DTMF Remote
No Connection

---
SUMMARY
SUMMARY
The world’s expectation is crystal clear wireless communications any time, any place.
  - In the Swiss Air crash, even amateurs would turn to cell phones if the radio link was noisy.
The technology exists and is available to Amateur radio to implement solutions that provide the coverage and audio quality required.

---
www.emrg.ca
The EMRG web site provides information related to Amateur radio emergency communications, specifically as it relates to the City of Ottawa.
Project Information
Newsletters
Upcoming Events
Documentation
Links to related information
Information: