EMRG-{xxx}
Data Communications
EMERGENCY MEASURES RADIO GROUP
OTTAWA ARES
Two Names - One Group - One Purpose
Amateur Radio Data Communications
APPLICATIONS
Date Of Last Change: 2008-01-11
Version: 1.1

---
Winlink 2000
Winlink 2000
Winlink 2000 is an Email System made up of 3 components;
Client Applications
HF Pactor
Airmail
Outpost
Email
Paclink
VHF/UHF Packet
Internet
CMS
Common Message Server
Perth Australia
CMS
Common Message Server
San Diago USA
CMS
Common Message Server
Halifax Canada
Email Servers
PMBO
Radio Message Server
RMS Pactor
RMS Packet
Telpac
Radio Message Server
RMS Packet
EPMBO
Radio Message Server
RMS Pactor
RMS Packet
RMS Relay
Radio Gateways

---
TYPICAL WINLINK SYSTEM
TYPICAL WINLINK SYSTEM
Client Applications
Radio Gateways
Airmail
Outpost
EPMBO
Radio Message Server
RMS Packet
RMS Relay
Telpac
Radio Message Server
RMS Packet
VHF/UHF Packet
Internet
CMS
Common Message Server
Perth Australia
CMS
Common Message Server
San Diago USA
CMS
Common Message Server
Halifax Canada
Email Servers
Email
Paclink

---
WINLINK LIKE AN ISP
WINLINK LIKE AN ISP
User A
Internet
User C
User D
User B
MY ISP
Mail Server
Mail Server
Mail Server
Telpac
Airmail
Packet Radio
Paclink
Email
Wired, DSTAR
or WiFi connection
WINLINK
CMS
Perth Australia
CMS
San Diago USA
CMS
Halifax Canada

---
WINLINK TO “MY ISP”
WINLINK TO “MY ISP”
User A
Internet
WINLINK
MY ISP
CMS
Perth Australia
Mail Server
CMS
San Diago USA
Mail Server
Telpac
User D
CMS
Halifax Canada
Mail Server
Packet Radio
Airmail
Paclink
Email
Wired, DSTAR
or WiFi connection

---
WINLINK TO ANY EMAIL
WINLINK TO ANY EMAIL
TEXT MESSAGING
10 digits@txt.bell.ca
10 digits@pcs.rogers.com
10 digits@msg.telus.com
User A
Internet
WINLINK
CMS
Perth Australia
CMS
San Diago USA
Telpac
CMS
Halifax Canada
Packet Radio
Airmail
Paclink
Email
Wired, DSTAR
or WiFi connection

---
DSTAR & WiFi
DSTAR & WiFi
DTAR or WiFi
Client Applications
HF Pactor
Airmail
Outpost
Email
Paclink
DTAR or WiFi
VHF/UHF Packet
Internet
CMS
Common Message Server
Perth Australia
CMS
Common Message Server
San Diago USA
CMS
Common Message Server
Halifax Canada
Email Servers
PMBO
Radio Message Server
RMS Pactor
RMS Packet
Telpac
Radio Message Server
RMS Packet
EPMBO
Radio Message Server
RMS Pactor
RMS Packet
RMS Relay
Radio Gateways
Paclink

---
TELPAC
TELPAC
Telpac is a Telnet to Packet gateway that provides a link between VHF/UHF Packet and the CMS Email servers, via the internet.
Radio Message Server (RMS) Packet is the new application that will replace Telpac.
Telpac can connect directly to a TNC or share a TNC through AGW Packet Engine.
TNC
Radio
Telpac
Internet Access

---
TELPAC GATEWAY
TELPAC GATEWAY
Airmail
The Telpac gateway does not process the information, it just acts as a protocol interface between Packet AX25 and TCP/IP Telnet.
Internet
CMS
Common Message Server
Perth Australia
CMS
Common Message Server
San Diago USA
CMS
Common Message Server
Halifax Canada
Email Servers
Telpac
Radio Message Server
RMS Packet
Airmail
Packet

---
PMBO
PMBO
PMBO refers to a publicly available station that provides HF Pactor and Packet gateway capability. The PMBO connects to the CMS Email servers via the internet.
This is the gateway used for HF Winlink connections.
Radio Message Server (RMS) Pactor and RMS Packet will replace the existing PMBO software.

---
EPMBO
EPMBO
An EPMBO is a PMBO that is dedicated to emergency communications, so it is not listed for public use
The EPMBO contains an additional software module that provides local message routing if the Internet connection is lost.
RMS Relay is the name for the new local message routing module.

---
AIRMAIL
Airmail is a standalone email client written specifically for Winlink. It provides an intuitive email like user interface. There are a number of modules that can be configured and run simultaneously to provide TNC access, HF access, SMTP server, etc.
Will run on Windows 95 or higher, with low power PC.
Does not support AGWPE (TNC is dedicated to Airmail, no sharing of TNC with other applications).
Supports attachments from Airmail directly or from external email program

---
Airmail
HF Forwarding
EMAIL
TNC
Internet
IP Network
Can connect directly through the Internet
Can provide a simplistic stand alone capability for direct Airmail to Airmail access, but does not allow the use of SSID in the callsigns.
Can provide message forwarding from VHF/UHF to HF.
Use of SMTP server to allow external email access, has configuration challenges.
Pactor 3
HF
SMTP
TNC
Radio

---
AIRMAIL SMTP SERVER
AIRMAIL SMTP SERVER
PC With Airmail & Email Client
TNC
Option to have all emails leaving Airmail will use the base callsign of Airmail, regardless of the callsign address used in the Email Clients.
SMTP server has options so it can send all Outgoing email to all users and all Incoming email to all users.
TNC
Radio
Airmail
Client
SMTP
Server
EMAIL Client
EMAIL
IP Network
Remote PC With Email Client

---
PACLINK
Paclink is an Email to Packet gateway allowing one or more email programs, such as Outlook, Outlook Express, or Thunderbird, to communicate with the Winlink system directly through the Internet, or a Telpac gateway.
Users have standard email interface and do not see the packet system, making it ideal for client sites.
Preferably a Win2K or higher PC.
TNC
Radio
Paclink
Email Client
TNC
Radio
Telpac
Internet Access
Basic Paclink – Direct TNC Connection

---
PACLINK
Supports attachments from external email program
Currently 2 programs, one provides email interface for which can connect directly to a TNC. The second program provides an AGWPE interface for Paclink. Being replaced with a single application called PaclinkMP.
A
G
W
P
E
TNC
Radio
IP NETWORK
Paclink
Loopback Port
EMAIL Client
WiFi &/or Wired IP Network
Gateway Computer
Multiple End User Computers
Multiple Users With Computer Network

---
OUTPOST
OUTPOST
Windows-based packet message client that can send and receive packet messages with almost any Amateur Radio Bulletin Board System (BBS) or TNC Personal Mail Box.
Designed for the ARES/RACES packet user community.
Runs on windows 95 or higher PC
Looks like an email client with similar functions such as create, send, receive, read, delete, reply to, or forward
Interprets the information sent from the TNC and BBS, automating the keyboard entry and interpretation performed by the user.

---
OUTPOST EXAMPLES
OUTPOST EXAMPLES
TNC
Radio
OUTPOST
TNC
Radio
Point to Point Connection
OUTPOST
TNC
Radio
OUTPOST
TNC
Radio
BBS or Telpac
Internet Access
BBS or Telpac Connection

---
OUTPOST & KPC3+ BBS
OUTPOST & KPC3+ BBS
Message from source to destination in 2 hops
OUTPOST
Radio
OUTPOST
KPC3+ TNC
Digi/Node
BBS
TNC is Digi/Node & BBS
Located at radio site
Remote access for config or reset
Simultaneous multi user access
OUTPOST
TNC
Radio
TNC
Radio
TNC
Radio
1
2

---
OUTPOST WITH AGWPE
OUTPOST WITH AGWPE
Gateway Computer
A
G
W
P
E
OUTPOST
TNC
Radio
Loopback Port
IP NETWORK
OUTPOST
WiFi &/or Wired IP Network
Multiple End User Computers

---
AGW PACKET ENGINE
(AGWPE)
AGWPE is an application that interfaces with one or more TNCs and/or Sound Cards, for AX25 Packet.
Presents a series of virtual TNCs to other applications, allowing sharing between multiple applications on a computer and between computers on a network.
With AGWPE, Paclink, Telpac and Outpost can all exist on the same PC and share a single TNC. Certain applications on other computers can share a TNC on another computer, over a network.
By installing AGWPE on multiple PCs on a network, TNCs can be shared across the network, or the Internet.

---
AGWPE APPLICATIONS
TNC or Soundcard
A
G
W
P
E
AGW Digi
All TNCs operation in KISS Mode.
AGW Terminal
Winpack
UISS
AGW Terminal
Outpost
TNC
Radio
UISS
AGW Terminal
Outpost
IP NETWORK
Paclink
Email Client
Other Bands or Speeds
TNC
Radio
TCP/IP
TNC
Radio
Telpac
Internet Access
APRS
TNC
Radio
WinAPRS
WinAPRS
A
G
W
P
E
Loopback Port

---
KPC3+ MUTI-USER BBS
KPC3+ MUTI-USER BBS
Kantronics KPC3+ (Version 9.x) has multi-user BBS functionality, allowing multiple users to upload - download messages at the same time.
Works well with Outpost using default config
Messages are stored based on the TO callsign, or a tactical callsign such as EOC.
Standard memory is 100K for mail out of 128K.
  - There is a modification (not tested yet) that allows the 128K memory to increase to 512K, providing about 480K for mail
TNC can be portable or located in remote radio site
Cost about $250

---
TACTICAL ADDRESSES
TACTICAL ADDRESSES
Tactical callsigns uniquely identify a site and apply to the site for the duration of the incident, while the user callsign may change over time.
BBS and Winlink both support tactical callsigns;
  - BBS = 6 Characters, Winlink = 12 Characters
Tactical calls can be set up on the fly, but there is value in defining them in advance, so they are standardized, then set up and tested.
  - Shelters would use site names for voice, such as Orleans Sportsplex. These are typically too long for data and can change, so a set of predefined standard identifier such as Shelter 1 would be useful for data.

---
TACTICAL ADDRESSES
Tactical callsigns must be unique, within the BBS and within Winlink. Since Winlink is a global system, the format must ensure uniqueness.
There are several proposals for Winlink tactical addresses, but there is no standard at this time.
The following proposed format will support both a BBS and Winlink; xxxxxxMMPPCC
  - xxxxxx – 6 character site identifier (Applies to BBS & Winlink)
  - MMPPCC - 6 character location identifier (Unique within Winlink)
    - MM - 2 character Municipality identifier
    - PP – 2 character Province identifier
    - CC – 2 character Country identifier

---
CONFIGURATION
CONFIGURATION
All of the software and hardware has options that can be used, or not used, with configuration settings that can be optimized.
Much of the documentation for the applications is volunteer written, so it is vague or has holes.
Implementing a data solution requires a lot of digging, trial and error and testing.
Any use of Email Clients or computer networking requires IP addressing, which must be planned in advance.