EMRG-{xxx}
Data Communications
EMERGENCY MEASURES RADIO GROUP
OTTAWA ARES
Two Names - One Group - One Purpose
Amateur Radio Data Communications
DEMO NETWORK
Date Of Last Change: 2008-01-11
Version: 1.1

---
PURPOSE
PURPOSE
The purpose of the Technology Demo is to show people some of the things that EMRG is working on, and some ideas that are possible based on available technology .
Hopefully some people will take some of these ideas, or get ideas of their own, and experiment to find solutions that can be applied to EMRG problems.

---
BASIC DATA COMMUNICATIONS Outpost & TNC BBS
BASIC DATA COMMUNICATIONS
Outpost & TNC BBS
Message from source to destination in 2 hops
OUTPOST
Radio
OUTPOST
KPC3+ TNC
Digipeater
& BBS
TNC is a Digipeater & a BBS
BBS located at radio site to reduce the number of hops
Remote access to TNC for configuration or reset
Simultaneous multi user access
OUTPOST
TNC
Radio
TNC
Radio
TNC
Radio
1
2

---
OUTPOST WITH AGWPE
Gateway Computer
A
G
W
P
E
OUTPOST
TNC
Radio
Loopback Port
IP NETWORK
OUTPOST
WiFi &/or Wired IP Network
Multiple End User Computers

---
AGWPE APPLICATIONS
145.030 MHz
Outpost
Operator Position 1
Outlook
Express
UHF Option
IP NETWORK
A
G
W
P
E
PaclinkMP
Outpost
Operator Position 2
RMS Packet
VA3OCE-1
APRS Option
Outlook
Express
RMS Relay
Outpost
Operator Position 3
Gateway Computer
VA3OCE
Outlook
Express
Internet Access
AGW Terminal
TNC
Radio
Loopback Port
TNC
Radio
TNC
Radio

---
Winlink 2000
Winlink 2000 is an Email System made up of 3 components;
Client Applications
Airmail
Outpost
Email
PaclinkMP
VHF/UHF
Packet
Internet
CMS
Common Message Server
Perth Australia
CMS
Common Message Server
San Diago USA
CMS
Common Message Server
Halifax Canada
Email Servers
PMBO
Radio Message Server
RMS Pactor
RMS Packet
RMS Packet
Radio Message Server
EPMBO
Radio Message Server
RMS Pactor
RMS Packet
RMS Relay
Radio Gateways
HF Pactor
HF Pactor
Telnet
Telnet

---
TYPICAL WINLINK SYSTEM
Radio Gateways
Email Servers
Client Applications
CMS
Common Message Server
Perth Australia
Airmail
CMS
Common Message Server
San Diago USA
VA3OCE-1
Radio Message Server
RMS Packet
RMS Relay
Telpac
Radio Message Server
RMS Packet
Email
Paclink
CMS
Common Message Server
Halifax Canada
Email
CMS
Common Message Server
Washinton USA
VHF/UHF Packet
Internet

---
WINLINK LIKE AN ISP
User A
Internet
User C
User D
User B
MY ISP
Mail Server
Mail Server
Mail Server
Telpac
Airmail
Packet Radio
Paclink
Email
Wired, DSTAR
or WiFi connection
WINLINK
CMS
Perth Australia
CMS
San Diago USA
CMS
Halifax Canada

---
WINLINK TO “MY ISP”
User A
Internet
WINLINK
MY ISP
CMS
Perth Australia
Mail Server
CMS
San Diago USA
Mail Server
Telpac
User D
CMS
Halifax Canada
Mail Server
Packet Radio
Airmail
Paclink
Email
Wired, DSTAR
or WiFi connection

---
WINLINK TO ANY EMAIL
TEXT MESSAGING
10 digits@txt.bell.ca
10 digits@pcs.rogers.com
10 digits@msg.telus.com
User A
Internet
WINLINK
CMS
Perth Australia
CMS
San Diago USA
Telpac
CMS
Halifax Canada
Packet Radio
Airmail
Paclink
Email
Wired, DSTAR
or WiFi connection

---
DSTAR & WiFi
DTAR or WiFi
Client Applications
HF Pactor
Airmail
Outpost
Email
Paclink
DTAR or WiFi
VHF/UHF Packet
Internet
CMS
Common Message Server
Perth Australia
CMS
Common Message Server
San Diago USA
CMS
Common Message Server
Halifax Canada
Email Servers
PMBO
Radio Message Server
RMS Pactor
RMS Packet
Telpac
Radio Message Server
RMS Packet
EPMBO
Radio Message Server
RMS Pactor
RMS Packet
RMS Relay
Radio Gateways
Paclink

---
Voice over IP (VoIP)
The system is made up of 2 ii3 VoIP Intercom units, configured for Peer to Peer mode, with one as a Client and the other as a server.
RADIO
F
SUI
M
Wired &/or
WiFi LAN
Console
(Client)
F
VoIP
Remote
(Server)
M
VoIP
Voice over IP
Standalone Audio Interface
LD1

---
RS232 Serial Extension
RS232 Serial Extension
RS232
Serial Communications
RS232 Over Ethernet
Wired &/or
WiFi LAN
TNC
Data

---
Sealed Buildings
Computers Inside, while Radios & “Appliance” Devices are Outside
SUI
Wireless Access Point/
Repeater
Wireless Bridge
Wireless Bridge
Voice
TNC
Data
LAN Switch
LAN Switch
VoIP
RS232
VoIP

---
POWERING THE LAN
POWERING THE LAN
DC-DC Converter
12VDC to 5VDC
12 VDC
Power Supply
Battery Backup
POE Injector
LAN Switch
Wireless Access Point/
Repeater
Wireless Bridge
Wireless Bridge
12 VDC
Power Supply
Battery Backup
LAN Switch

---
POWERING THE LAN
Wireless Access Point/
Repeater
Wireless Bridge
DC Power Supply
12VDC to 5VDC
12 VDC
Power Supply
Battery Backup
SUI & VoIP
Laptop
POE Injector
12 VDC
Power Supply
Battery Backup
LAN Switch

---
Power Over Ethernet (POE) 12 VDC Power Injector
Power Over Ethernet (POE)
12 VDC Power Injector
RJ45 Plug - T568A
DATA & 12VDC
POE
1
white/green
green
white/orange
blue
white/blue
orange
white/brown
brown
8
Tab is on back side of plug
8
1
1A
(ATO)
12VDC
Powerpole
DC Power Connector
GROUND
+12 VDC
4 6 8 7
5 3 1 2

---
Power Over Ethernet (POE) 5 VDC Power Supply
Power Over Ethernet (POE)
5 VDC Power Supply
Heatsink
D1
6A 100V
U1
7805
3
1
Coaxial DC Power
OD: ID:
2
+
5VDC (600MA)
+
C2
100uf
50V
C3
0.1uf
60V
C1
100uf
60V
D2
36V
5W
F1
2A 32V
DATA & 12VDC
POE
12VDC
RJ45 Plug - T568A
1
white/green
green
white/orange
blue
white/blue
orange
white/brown
brown
8
Tab is on back side of plug
1
8
2 1 3 5
7 8 6 4

---
DEMO STATIONS
VE3ECN@winlink.org
VE3ECN - DEMO1
VA3OCE
Outpost
EMAIL Client
VA3OCE@winlink.org
VA3OCE - DEMO2
VA3OCE
Station 1
TNC
Radio
Airmail
TNCx
Radio
192.168.1.100
AGWPE
Station 2
Internet
Winlink
Mail Servers
TNC
Radio
RMS Packet
VE3BQP-1
AGWPE
VE3BQP Home Station
145.030 MHz
TNC
Radio
DIGI: VE3OCE
NODE: VE3OCE-2
BBS: VE3OCE-1
Wireless Access Point
IP NETWORK
Outpost
EMAIL Client
PaclinkMP

---
VE3BQP Home Station
DEMO STATIONS
145.030 MHz
AGWPE
RMS Packet
VE3BQP-1
Internet
DIGI: VE3OCE
NODE: VE3OCE-2
BBS: VE3OCE-1
Winlink
Mail Servers
Station 1
VE3ECN@winlink.org
VE3ECN - DEMO1
VA3OCE
Airmail
Outpost
EMAIL Client
Wireless Access Point
IP NETWORK
Station 2
AGWPE
192.168.1.100
VA3OCE@winlink.org
VA3OCE - DEMO2
VA3OCE
PaclinkMP
Outpost
EMAIL Client
TNC
Radio
TNCx
Radio
TNC
Radio
TNC
Radio